## Slide 1: I want to deploy and SBC and my security laughed at me…

## Slide 2
Chris Clauss
Manager, Avaya UC
Engineering
John Waber
Training Development
Manager

## Slide 4: Let’s have fun together…
Thanks for coming!
Please ask questions!
Let’s make this time together worthwhile!

## Slide 5: Topics
Workplace Client Overview
Aura Requirements
Customer Requirements
Device Services
VDI Requirements
Call Center Features
Rock Solid Performance

## Slide 6: Adding and SBC and Security
SBC for remote worker adds significant security implications to the network.
Not a simple bolt on applications. Requires help from
  Security Team
  Certificate / TLS Team
  DNS administrators
  Firewall / Network Team

## Slide 7: How do we check the boxes?
Security teams will ask question and drive requirements of your deployment. Be prepared to address.
Certificates
Authentication
Application Relay
Firewalls
Virtualization

## Slide 8: Avaya Enterprise SBC
SBC is a security appliance
Avaya hardened solution
Special purpose firewall
SIP and RTP aware for traversal of signaling and media.
Proxy of services between trusted and untrusted zone.
Application proxy to allow other services (HTTPS Utility / Presence / PPM)

## Slide 9: Avaya Enterprise SBC Roles
SIP Trunking
Connecting enterprise network to carrier to support SIP trunking
Remote Worker
Securely connect remote workers using physical phones or softphone applications
Application Proxy
Securely provide application proxy for services that fall outside SIP.

## Slide 10: SIP Trunking
Provide a connection to carrier for SIP trunking
Carrier connection for SIP trunking is usually on a dedicated circuit provided by the carrier.
Carriers sometimes indicated that you do not need an SBC because they provide one. Bad security idea – no network demarcation.
Bring your own bandwidth (BYOB) carriers connect via internet.
Third party service provides over dedicated link or via internet.
SIP Trunking

## Slide 11
Provide remote workers to use their phone from anywhere.
No VPN required as SBC handles the security.
Only allows voice traffic to flow when user is authenticated.
SIP only.
Supports both physical endpoints (96xx/J1xx) and Avaya soft clients.
Remote Worker

## Slide 12
Supports applications other than SIP / RTP. Common applications include:
HTTP / HTTPS proxy of Utility server to allow physical phones to get 46xxsettings file.
HTTPS web services of Avaya Aura Device Services (AADS) to provide auto configuration of Avaya Workplace softphone and Agent for Desktop
HTTPS web service to provide Web Licensing Manager (WebLM) access for applications.
PPM / Presence Proxy
Application Proxy

## Slide 13: SBC Hardware / Software
SBC can be deployed on physical servers or virtualized.
Physical server often chosen as SBC usually placed in DMZ – easy to “see” network interfaces.
Can run on virtual platforms (VMWare / Azure / AWS) – must be very careful to properly configure network interfaces.
If running VM, consider a DMZ host.

## Slide 14: SBC Interfaces
Public Interface – Unsecure
Private Interface – Secure
Management Interface – Out of Band / often on same subnet as
private interface

## Slide 15: Adding SBC to your Enterprise.
Understanding SBC Topology is important to deploying the unit in a secure way.
Security is best applied in a layered approach, with no single device responsible for end-to-end security.
SBC device pairs can also be configured for high availability

## Slide 16: SBC – Simple Install – SIP Trunk Only
Leased Line
Leased Line to Carrier Network
Carrier network often “trusted”
SBC provides a demarcation.

## Slide 17: SBC – Simple Install – Remote Worker
SBC acting as the firewall
Provides secure access for remote workers
No “layered” security.

## Slide 18: SBC – Behind Firewall – Remote Worker
SBC behind firewall.
Provides secure access for remote workers
Adds layered security.
Firewall should not inspect SIP / do ALG. Just pass / block traffic.

## Slide 19: SBC – In DMZ – Remote Worker
Most common deployment.
Provides secure access for remote workers
Adds layers of security / separation.
Firewall should not inspect SIP / do ALG. Just pass / block traffic.
SBC is aware of firewall and will rewrite NAT changes.

## Slide 20: SBC – Avoid Interfaces on same subnet
Never
Place both secure and unsecure interfaces in same subnet.
Allow direct routing between secure and unsecure interfaces.

## Slide 21: SBC – Use separate SBCs
Put SIP trunks on one SBCE and Remote Users on another
SIP trunking does not require much tweaking, once it is set up. Configuration mistake could affect whole company.
Remote worker might require tweaking frequently. Configuration mistake would affect a sub-set of the company
With most company’s Change-Management rules, getting permission to modify the SBCE running SIP trunking is more difficult than modifying remote worker rules.
Adds layers of security.

## Slide 22: SBC PORTS AND PROTOCOLS

## Slide 23: SBC Topology for Remote Worker

## Slide 24: Authentication of Endpoints
Most important thing to remember in this presentation!
SBC authenticates all endpoints using SIP username and SIP station password.
By default, SBC will authenticate a user if username and password are valid.

## Slide 25: Authentication of Endpoints
One SBC is internet connected, look for probes and registration attempts within about 5-10 minutes.
Hackers will attempt registration with sequential logins to stations using common passwords – station number / 1234 / 9999 / station number backwards.
Do all your SIP endpoints have secure passwords?

## Slide 26: Case in point
What was the first SIP endpoint in your business?
Customer added remote worker.
Configured secure SIP passwords for the remote workers.
Forgot about the other endpoints.
Conference room phone with simple password led to toll fraud!

## Slide 27: But Workplace uses network credentials, right?
Avaya Workplace leverages Avaya Aura Device Services (AADS) for single sign on.
Important to understand that AADS provides SSO, and authenticates the user as valid, but then pulls SIP login and password from Session Manager and sends it back to the phone to login to the SBC.

## Slide 28: Authentication of Workplace
Workplace can leverage AADS to authenticate. AADS in turn can validate user logins
Workplace send credentials to AADS to be validated with LDAP.
AADS can redirect Workplace to a SAML provider for more secure authentication or two factor authentication
Is SAML authentication a requirement for your organization?

## Slide 29: Avaya Aura Device Services Authentication
AADS
LDAP/SAML
System Manager
Session Manager Data
1
2
3
4
6
5
User enters their LDAP/AD Credentials. Workplace sends it to AADS for authentication.
AADS asks LDAP/SAML if the user credentials are valid.
LDAP/AD looks up the user and checks credentials and groups, replies to AADS.
If the user is authorized, AADS will match a user in System Manager and pull SIP login information from Session Manager database.
SM will look that up in PPM and pass it back to AADS.
AADS will dynamically create a one-time use settings file for that user that includes, among other things,
SET SIPUSERNAME ”user’s_ext”
SET SIPPASSWORD ”user’s_pw"

## Slide 30: Authentication of Endpoints
Physical endpoints always use SIP station and password to login via the SBC.
SIP password should be…
Secure
Alphanumeric
Long
Contain Special Characters
If using only digits as an accommodation – make it very long

## Slide 31: Passwords for RW
Weak telephone passwords are a direct path to toll fraud.
A 4-digit pin (0000-9999) can be hacked in 142 seconds.
A 5-digit pin (00000-99999) can be hacked in 8 minutes.
A 6-digit pin (000000-999999 can be hacked in 9 hours.
A 7-digit pin (0000000-9999999) can be hacked in 6 days.
An 8-digit pin (00000000-99999999) can be hacked in 3 weeks.

## Slide 32: Password Security using System Manager
Did you know System Manager provides self service password configuration for end users?
https://smgr/selfprovisioning
Works best if SMGR users are synced with corporate directory.
Supports password changes & expiry for Agent and Messaging as well as h.323 and SIP, but only supports password aging for SIP profile.

## Slide 33: Password Security using Password Pro (C1)
C1 provides Password Pro
Add on product that provides enhanced features for use self service.
Password Pro can
Support password aging and complexity
Both h.323 and SIP stations.
Supports windows login / SSO / SAML
Much more streamlined, with fewer steps for configuration and setup.
Management status of expirations for all users.
Let you specify the action taken for warnings and expirations (None, Warning-only, Auto-reset) on individual users.

## Slide 34: How do we enhance security?
Besides strong passwords…
Enforce User Agents
User URI Groups
Use TLS encryption everywhere.
Separate SBC for Trunk and Remote Worker
Enforce Mutual Authentication
Futures

## Slide 35: Blocking hackers with User Agent
SBC can identify the “model” of software trying to register as a remote worker.
SBC can ignore requests from devices that are not identified as Avaya devices.
Eliminates “script kiddies” that are trolling SBC.
Hackers are aware of this and will masquerade as Avaya endpoints.

## Slide 36: Blocking hackers with URI Groups
Do this for every install!
Specify number / list of numbers / regular expression for remote workers.
Only those matching list will be allowed to register.
Does require additional administration.
Blocks phones that are not meant to be remote worker.

## Slide 37: TLS Encryption
TLS must be used on public interface of SBC, otherwise traffic can be captured, eavesdropping of calls can take place, and passwords compromise.
Recommend that SIP signaling be encrypted end to end on internal network as well. RTP media can be converted to non-encrypted by SBC for internal network. May be required for call recording.
Session Manager will always default to TLS over TCP/UDP if possible.
Unencrypted
Encrypted

## Slide 38: TLS Authentication
Mutual Authentication provides a mechanism that enhances security of TLS encrypted sessions between systems.
By default, Avaya endpoints do not use mutual authentication. The endpoint will validate the SBC certificate
The Server will not require the client to present a certificate.
Much like most web sites – only login / password are required.

## Slide 39: TLS Mutual Authentication
When mutual authentication is enabled on the server, the client must also send an identity certificate to the server. The client validates the server certificate, and the server validates the client certificate. If either validation fails, TLS negotiation fails.

## Slide 40: Why is Mutual Authentication problematic?
To do mutual authentication, each device needs an identity certificate.
Certificates must be distributed to devices / soft phones.
System Manager can be used a SCEP server for phones starting in 8.1.3+
SCEP or
MDM
Server

## Slide 41: Certificate Distribution - Phones
Phone can request a cert from SCEP servers via 46xxsettings file.
MYCERTURL = x.x.x.x IP address for the SCEP server MYCERTCN = $serialno Use the serial number as client ID. MYCERTDN = Geographic identity of the customer’s domain for example: /C=US/ST=NJ/L=Oakland/O=clauss.org MYCERTKEYLEN = 2048 MYCERTRENEW = 730 set to the period of renewal. MYCERTWAIT = 1 wait for a certificate. SCEPPASSWORD = $SERIALNO or SCEP server password
Since SCEPPASSWORD is in clear text in settings file and anyone can download it, Avaya recommends adding certs to phones using a staging network.
Another option is to use the same certificate for all phones. Cert is sent to the phone as PKS12 file and password must be entered on the set.
SCEP
Server
SCEP
REQUEST
REPLY
WITH CERT

## Slide 42: Certificate Distribution – Windows / MAC
Desktop computer can be provided with identity certs via group policy or other device management tools.
Certs can also be added manually.
Workplace client has an option to select which cert to use for client authentication.
End user must select certificate to be used.

## Slide 43: Certificate Distribution – IOS / Android
IOS and Android devices limit an applications ability to select a client certificate (security limitation of operating system).
Process to add an identity certificate for mobile devices is the same as physical phones.
Client must be able to connect to SCEP server to obtain a certificate – hence staging network / VPN / bring phone in house.
SCEP
Server
SCEP
REQUEST
REPLY
WITH CERT

## Slide 44: Another problem with Mutual Authentication?
Certificates Expire
Near expiration, phones will warn of identity certificate expiration.
Phones / Softphones must be brought back to staging network for new certificate.
SMGR 8.1.3+ has new options to regenerate a certificate for physical phones but must be accessible to endpoint (problem for remote worker – SMGR proxy).

## Slide 45: Certificate Revocation
A certificate issued to a phone can be deleted from the phone using the DELETE_MY_CERT setting. Care must be taken to apply this setting only to specific phones. This setting can be applied in the settings file to a group, or to a specific MAC address or Serial Number.
SBC will honor Cert Revocation List (CRL) if configured.

## Slide 46: Additional Recommendations
Disable TLS 1.0 / 1.1 - Inherently secure and cracked.
Do not use SHA1 for certificates – cracked.
Do not use Avaya demo certificates – anyone can access using these.
Remember that certificates must meet Apple / Google requirements for mobile devices. 2048 bit / SHA2 / Include SAN / 825-day validity.

## Slide 47: Future Enhancements to the SBC
Avaya recognizes the importance for securing a remote worker SIP solution. Upcoming releases of SBC software will include the following features.
Blacklisting IP addresses that have several failed password attempts. This will block the ability for any station to login from a specific IP address.
Syslog alerting when an attack is in place.

## Slide 48: Future Enhancements to the SBC
48
48
48
Edge Gateway Services
Allows h.248 Gateways in remote locations to connect to core via SBC.
Secure TPKT Transport (ISO over TCP)
TLS Ports 2944/2946
Mutual Authentication required.
Remote analog and digital stations.
Branch #1
NAT Address Space 1
NAT’d Address Space 2
Public
WAN Address Space
DCP
Analog
MGSBC TCP 2946
H.248 Link TCP 2944
Branch #2
DCP
Analog
SIP
SIP
Static IP Address pair (public/private)
Single Public Address with dynamic NAT
Enterprise Data Center
Enterprise Address Space
MGSBC TCP 2946
H.248 Link TCP 2944

## Slide 49: System Manager as Certificate Authority
Pros
Works out of box
Automatically issues and deploys and redeploys certificates for managed elements (SMGR / SM)
Aura environment stands alone
Cons
PKI is independent of other PKI
No enterprise branding
Must distribute PKI to endpoints
Simplest management for Aura certificates

## Slide 50: Enterprise Private CA / Public CA
Pros
Provide enterprise asserted trust
Certificates may already be distributed to client devices.
Cons
Must manually establish PKI trust chain to Aura managed devices.
Must create Certificate signing request and import identity certificates
No automatic issue or re-issue of certificates.
Relatively straightforward deployment. Not require for all devices. (Can generate identity certs only for required)

## Slide 51: SMGR as Subordinate CA to Enterprise CA
Pros
Provides enterprise certs.
Certificates may already be distributed to client devices.
Automatically issues and deploys and redeploys certificates for managed elements (SMGR / SM)
Cons
Enterprise must allow sub-CA
Trust chain must be distributed to all Aura elements
Difficult to implement.

## Slide 52: Questions to ask to keep Security Happy
What to ask your security / firewall team?
What Certificate Authority must we use?
Can we implement softphones and hard phones?
What type of authentication do we need for softphones – LDAP / SAML?
Do we need to use mutual authentication?
Do we revoke certificates using CRL?
Do we have a SCEP / NDES server?
Is HTTP allowed for configuration of phones?

## Slide 53: In Summary
You must use secure SIP station passwords.
Avaya SBC is a robust security device.
Can be deployed in a topology to make firewall team happy.
Can adapt to provide security features to keep security team happy.
Add layers of security – multiple firewalls / SBCs.
You need to discuss the implementation with the teams in your enterprise or your project could get stopped.
Understand the special requirements for remote workers including authentication, certificates, and additional security features in the SBC.
Most important…

## Slide 54: What’s the best way for you to get help these configurations?
Come ask us questions
www.convergeone.com
Thanks for attending!
Chris Clauss
cclauss@convergeone.com
Find the best partner – here at the show! Please fill out your session survey!
Please tweet about the presentation if you liked it – @clauss
John Waber
jwaber@convergeone.com
Get this presentation – https://www.clauss.org