## Slide 1: Hybrid Cloud - Adding Cloud Services to Your Enterprise PBX

## Slide 2
Manager, Avaya UC Engineering
Collaboration
ConvergeOne
Chris Clauss

## Slide 3
ConvergeOne
Feel The Impact
Notes: ConvergeOne is an IP Enabled, services led technology company which provides a holistic environment for secure connected customer experiences for our clients.

## Slide 4: Visit our Other Sessions!

## Slide 5: Everyone is talking about cloud…
Many great reasons to move…
Ease of implementation
Adding new services
Exciting features
Subscription based
Many reasons not to move…
Transition is difficult
Need enterprise features
Call Center

## Slide 6: Avaya provides cloud services for “On Prem Customers”
Avaya Spaces
Included in subscriptions
Replaces on-prem systems for Conferencing
Adds Collaboration Capabilities
Avaya Spaces Calling
Bundled into Avaya Spaces
Offers a quick and easy way to add remote workers.

## Slide 8: Avaya Spaces – Conferencing – Let’s take a tour…
spaces.avayacloud.com
Good news – Avaya SSO supports linking to Enterprise SAML providers…

## Slide 9: My Meeting Room
A personal meeting room for every user.
Unique Room ID
Can join from browser phone
Can join from an Avaya Room System
Persistent Chat History & Posts
Task List
List of previous meetings and recordings

## Slide 10: My Meeting Room
Meetings can auto start.
Entry / Exit Tones
Waiting Room
Prevent Unmuting
AI Noise Removal (VERY COOL)
Remote Control (NEW at last)
Live Caption (English / Spanish)

## Slide 11: My Meeting Room
Very Large Meetings (250 / 1000)
3rd Party Room Systems (SIP)
  sip:xxxxxx@spacesip.net
Create Content – Post / Tasks
Video Layouts / Lecture
Video 360p to 1080p
Security – waiting room / password
Virtual background blur
Toll free access numbers

## Slide 12: What’s the point?
Feature parity with WebEx / Zoom
But some additional features…
I/M direct from Workplace app or Spaces Web interface – no Presence Server required.
Easy enterprise integration with Aura and Enterprise Directory
Office 365 Integration for Calendar

## Slide 13: And more…
A user can create additional spaces – each with all the same features.
Meetings can run on any browser.
Spaces also has a mobile and desktop client.

## Slide 14: Spaces is easy to manage
Users can be added via admin web interface, but let’s make a hybrid environment.
Manage Spaces from AADS.
Users will automatically be added based on LDAP (Active Directory) group management.

## Slide 15: But first – let’s associate our company so people can sign on…
https://accounts.avayacloud.com
Manage Companies
Add New Company
Add a domain
Verify the domain
Add DNS record so Avaya can confirm you control the domain.

## Slide 16: Now let’s configure AADS to add users automatically…
What is Device Services?
Provides auto configuration on Avaya Devices (Workplace and Phones)
Supports Single Sign on / SAML
Enterprise Directory
Updates clients
Auto configures Spaces users / Spaces SSO

## Slide 17: Space AADS Integration

## Slide 18: AADS Space Integration

## Slide 19: AADS Space Integration

## Slide 20: AADS Spaces Integration
Any users that are a member of the A/D (LDAP) group will automatically get a Spaces account.
Upon creation of a new account, email will be sent to a user to complete login.
Since Spaces supports enterprise login / SAML, end user admin is self service.

## Slide 21: Users automatically added to Spaces admin portal.

## Slide 22: Users can also be manually added

## Slide 23: How much more hybrid can we make it?
Spaces includes Spaces Calling.
Pure web based soft phone that works from browser. Supports basic calling features. Leverages Avaya Cloud Media Server – includes AI Noise Removal

## Slide 24: Spaces Calling
3 Options for Spaces Calling
Web Based Client – Browser based from Spaces Web Interface.
Chrome add on.
Workplace Client

## Slide 25: Spaces Web Client
Calls directly from web browser interface of Space.
Requires and additional component
Avaya Aura Web Gateway
Avaya Aura Media Server
Can leverage existing media server used for CM.
Does not require an SBC. Magic!
Leverages Avaya Cloud Media Services

## Slide 26: Spaces Web Client – no SBC needed!

## Slide 27: Spaces Chrome Add In
Zero client installer – can be added as a Chrome Extension.
Runs on and machine that Chrome runs on.
Requires and additional component
Avaya Aura Web Gateway
Avaya Aura Media Server
Does require Avaya SBC for remote worker.
Can leverage existing media server used for CM.

## Slide 28: Spaces Chrome Add In – SBC required for STUN/TURN/WebRTC Proxy

## Slide 29: Spaces Using Avaya Workplace
Full client for Windows / Mac / Mobile
Requires and additional component
Does require Avaya SBC for remote worker.
Spaces “pops” Workplace
Can leverage existing media server used for CM.

## Slide 30: Spaces using Avaya Workplace – Requires SBC

## Slide 31: Configuring Avaya Aura Web Gateway
What is the Web Gateway?
Swiss Army Knife for Avaya web-based applications.
Provided several legacy services for Apple Push Notification / Conferencing
Now provides Spaces Calling integration to Aura Enterprise
WebRTC to SIP gateway.

## Slide 32: Configuring Avaya Aura Web Gateway

## Slide 33: Configuring Avaya Aura Web Gateway – Generate and Export Key

## Slide 34: Copy configuration to Spaces Admin Portal

## Slide 35: Configure user settings.

## Slide 36: If using Space Calling extension for Chrome add App accounts.avayacloud.com
{
"Aura_Web_Gateway_Server_Profile":[
{ "Name": "Internal clauss.org", "Address": "v-aawg.clauss.org", "AccountsToken": true, "LogDownload": true, "DialRule": false
},
{ "Name": "External clauss.org", "Address": “sbc.clauss.org", "AccountsToken": true, "LogDownload": true, "DialRule": false
}
]}

## Slide 37: Server Roles
Avaya Aura Device Services
Ties together user configuration / LDAP services / System Manager.
Matches enterprise users to Avaya users in System Manager.
AAWG
Provides Web Services for Spaces Calling.
Media Server
Anchors media from Spaces Calling to Aura

## Slide 38: Tips and Pitfalls
Configuration is a bit scattered..
Spaces Calling Settings
spaces.avayacloud.com – admin portal – Settings – Avaya Spaces Calling
Company Settings – Adding a company
accounts.avayacloud.com – Manage Companies – Add
Company DNS configuration
accounts.avayacloud.com – select company / domains
Manual User
accounts.avayacloud.com – select company / manage users
Spaces Calling for Chrome
accounts.avayacloud.com – select company / Apps / add Avaya Spaces Calling

## Slide 39: Other options for cloud migration for enterprise customers
Avaya Enterprise Cloud hosted on Microsoft Azure. Moves enterprise Aura to an Avaya hosted solution.
Avaya Enterprise Cloud with C1. Avaya Aura hosted by ConvergeOne. Great scale and flexibility in customization.

## Slide 41: Questions / Comments / Applause / Boos…

## Slide 42: What’s the best way for you to get help settings all this up?
Come ask us questions
Call us – 888-777-7280
Check us out online – www.convergeone.com
Thanks for attending!
Chris Clauss
cclauss@convergeone.com
Find the best partner – here at the show! Please fill out your session survey! Session 1041
Please tweet about the presentation if you liked it - @clauss